## Slide 1: Analytical Techniques
Used to identify or compare matter
Different techniques exist for organic or inorganic substances
Most analysis in a forensic lab involves organic analysis

## Slide 2: Organic versus Inorganic
Organic: contains carbon
Inorganic: does not contain carbon

## Slide 3: Organic Functional Groups
A functional group has a characteristic structural feature or a unique arrangement
Carbon often bonds to hydrogen, oxygen or nitrogen
Functional groups are a group of atoms showing similar behavior in a chemical reaction (drug color tests) and absorb light at a particular wavelength (ex. IR spectrum)

## Slide 4: Organic Analysis
Nature of bonds in organic compounds can be easily characterized by their absorption of light
Spectrophotometry: study of the absorption of light by chemical substances
  Characterizes and identifies organic materials
To analyze a substance, it must be relatively pure

## Slide 5: Chromatography
Purifies substances
Separates and tentatively identifies components of a mixture
Useful for multi-component substances
Two phases: mobile phase moves, stationary phase is fixed

## Slide 6: Another look at chromatography:

## Slide 7: Most applicable types of chromatography
Gas chromatography
(GC)
High performance chromatography (HPLC)
Thin-layer chromatography (TLC)

## Slide 8: How chromatography works:
Generally a solid stationary phase and a mobile liquid or gas phase
Components with the greatest affinity for the mobile phase travel the farthest up the plate (TLC) or the fastest through the column (GC)

## Slide 9: To tentatively identify a component of a mixture
A known or standard reference sample is developed on the SAME plate as the unknown in TLC or run through the GC for comparison
Data has been published to aid in the choice of mobile and stationary phases

## Slide 10: Sample GC
Sample GC
A mixture of barbiturates
Retention time: time required for a component to emerge from injection
Courtesy of Varian Inc., Palo Alto, CA
Courtesy Varian Inc., Palo Alto, Calif.

## Slide 11: GC
Used to resolve highly complex mixtures into components quickly!
Can be used to tentatively ID a substance. Why?
Often paired
with a mass
spec.

## Slide 12: Figure 11–19 How GC/MS works. Left to right, the sample is separated into its components by the gas chromatograph, and then the components are ionized and identified by characteristic fragmentation patterns of the spectra produced by the mass spectrometer.

## Slide 13: Figure 11–20 (a) Mass spectrum of heroin. (b) Mass spectrum of cocaine.

## Slide 14: Figure 11–21 A tabletop mass spectrometer. (1) The sample is injected into a heated inlet port, and a carrier gas sweeps it into the column. (2) The GC column separates the mixture into its components. (3) In the ion source, a filament wire emits electrons that strike the sample molecules, causing them to fragment as they leave the GC column. (4) The quadrupole, consisting of four rods, separates the fragments according to their mass. (5) The detector counts the fragments passing through the quadrupole. The signal is small and must be amplified. (6) The data system is responsible for total control of the entire GC/MS system. It detects and measures the abundance of each fragment and displays the mass spectrum. Source: © Agilent Technologies, Inc. 2013 Reproduced with permission, courtesy of Agilent Technologies, Inc.

## Slide 15: Figure 11–12 (a) In thin-layer chromatography, a liquid sample is spotted onto the granular surface of a gel-coated plate. (b) The plate is placed into a closed chamber that contains a liquid. As the liquid rises up the plate, the components of the sample distribute themselves between the coating andthe liquid. The mixture is separated, with substances with a greater affinity for the moving liquid traveling up the plate at a faster speed.

## Slide 16: Figure 11–13 (a) The liquid phase begins to move up the stationary phase. (b) Liquid moves past the ink spot carrying the ink components up the stationary phase. (c) The moving liquid has separated the ink into its several components.

## Slide 17: Figure 11–14 Thin-layer chromatogram of a marijuana extract.

## Slide 18: Figure 11–15 Chromatograms of known heroin (1) and quinine (2) standards alongside suspect sample (3).