## Slide 1: Analytical Techniques
Used to identify or compare matter
Different techniques exist for organic or inorganic substances
Most analysis in a forensic lab involves organic analysis (chapter 5)

## Slide 2: Organic Analysis
Nature of bonds in organic compounds can be easily characterized by their absorption of light
Spectrophotometry: study of the absorption of light by chemical substances
  Characterizes and identifies organic materials
To analyze a substance, it must be relatively pure

## Slide 3: Spectrophotometry
The study of the absorption of light by chemical substances
Characterizes and identifies organic materials

## Slide 4: White Light
Upon passing through a prism, the light will separate into a spectrum of colors

## Slide 5: Color
Why does an object appear yellow?
  When white light passes through the object all colors are absorbed except for the yellow light.
  The yellow light is reflected by the object.

## Slide 6: The nature of light: 2 models
Light is a continuous wave
Light is a stream of continuous particles

## Slide 7: The wave nature of light
Wavelength (λ) = distance between two consecutive crests or troughs of a wave
Frequency (ν) = # crests or troughs passing a given point in a unit of time
  Units are cycles per second or Hertz (Hz)

## Slide 8: Wavelength and frequency
λ * ν = c
where c = speed of light in a vacuum = 3.00*108 m/s
As wavelength increases, frequency decreases
Different colors of light have different wavelengths and frequencies

## Slide 9: Electromagnetic Spectrum

## Slide 10: Once light is absorbed:
Light must now be described as discrete particles called photons.
Energy of a photon (E) = h * ν
The greater the frequency (ν), the greater the energy.

## Slide 11: Spectrophotometry:
Basic components:
Measures the quantity of radiation a material absorbs as a function of wavelength or energy

## Slide 12: Important light sources for forensics:
Visible, infrared (IR), ultraviolet (UV)
Generates a “fingerprint” for a substance

## Slide 13: Examples of spectrums
UV and visible spectrums are simple compared to IR spectrums, provide probable ID, TLC or GC confirms
UV spectrum of
heroin
Compare to
IR spectrum in
Figure 5-19

## Slide 14: Mass spectrometry
Sample is bombarded with high energy electrons
Positively charged ions form = cations
Cations are unstable, decompose to fragments, pass through an electric or magnetic field, separate based on mass

## Slide 15: Mass spectrum of heroin (top) and cocaine (bottom)

## Slide 16: Mass spectrometer
One of the most important tools in forensics
Sensitive to small concentrations
Widest use: drug identification

## Slide 17: GC Mass Spec
GC separate mixture, mass spec provides identification of mixture components
Under carefully controlled conditions, no two substances produce the same fragmentation pattern
  = fingerprint

## Slide 18: GC Mass spec.

## Slide 19: Web-extras
5.2 GC
5.5 Mass spec.