## Slide 1
Commercial Buildings Energy Assessment Program
Training Module 1.3
Units Used in Energy Assessments

## Slide 2
SI and IP Systems of Units
SI – “Metric” System is used in most countries
IP – “Inch-Pound” or English system is generally used in the US
HVAC – Uses a combination of SI and IP systems
Power Units
HP or Horsepower
kW or Kilowatt

## Slide 3
Converting Units
The equivalence between any two units can be written as a ratio.
1 ft = 12 inches
1 ft
12 inches
=
1
Equivalencies are referred to as
Unit Conversions
Examples:
12 inches = 1 ft
60 seconds = 1 minute
60 minutes = I hr

## Slide 4
Converting Units
Example:
Find the equivalence for the flow rate of water measured in units of lb/hr and gallons per minute (GPM).
Solution:
Density of water is 62.4 lb/ ft^3 (at 60 deg F)
7.48 gallons = 1 ft^3
1 gallon = 1 gal x 60 min x 1 ft^3 x 62.4 lb = 500 lb
minute min hr 7.48 gal ft^3 hr
Or 1 gpm (water) = 500 lb/hr