## Slide 1: Aircraft landing gear systems
Airframe 02

## Slide 2: Section Overview
Landing Gear Types
Jacking
Wheel Alignment
Retraction Systems
Shimmy Dampeners
Landing Gear Struts
Wheels
Tires
Brakes

## Slide 3: Landing Gear Types
Numerous Configurations
Fixed
Retractable
Non-Shock Absorbing
Shock Absorbing
Amphibious
Skiis

## Slide 5: Gear Arrangements
Tail Wheel
Known as conventional gear due to many early aircraft having this configuration
Main gear is located forward of center of gravity
Tail gear or skid
Facilitated clearance for large props
Good for non-paved surfaces
Weight saving due light tail wheel
Differential braking and steering

## Slide 6: Gear Arrangements
Tandem landing gear
Main and tail aligned on longitudinal axis
Some have outriggers

## Slide 7: Gear Arrangements
Tricycle gear
Most commonly used
Used on large and small aircraft
Two mains and a nose gear
Benefits include
Enables higher landing speeds
Better visibility from flight deck
Prevents ground looping of aircraft

## Slide 8: Nose Gear
Can be non-controllable
Most are controllable with linkage or hydraulics
Heavy aircraft use an independent tiller

## Slide 9: Main Gear
Attached to a reinforced wing structure
Number of wheels vary
Multiple wheels spread load and provide backup
Bogie is when more than two wheels attached to a strut

## Slide 10: Tricycle Gear Components

## Slide 11: Fixed and Retractable Gear
Fixed
Small aircraft
Parasite drag
Wheel fairings
Fixed vs. retractable weights
Faster aircraft need to retract gear
Aerodynamic designs
Retractable
Stows gear in fuselage
Can be used to slow aircraft

## Slide 12: Shock and Non-Shock Absorbing
Forces on aircraft during landing must be controlled
Either by transfer through the airframe or by converting energy into heat energy
Leaf spring type
Gear flexes and returns to normal
Made from composite materials, lighter and do not corrode
Rigid
Direct transfer to airframe
Tires cushion landing
Helicopter skids
Bungee Cord
On non shock absorbing gear
Made of elastic rubber

## Slide 13: Shock Struts
Used to convert the energy of impact to heat through dissipation
Self contained hydraulic units
Must be inspected and service routinely
Uses compressed air or nitrogen combined with fluid
Air/oil strut or OLEO
Telescoping
Metering orifice
Metering pin
Heat is dissipated through the strut assembly
Some struts use metering tubes rather than pins
Snubbers or dampeners extension stroke

## Slide 15: Strut Parts
Axle
Provides installation of aircraft wheels
Struts without integral axle have provisions
Valve fitting assembly
Provides means of servicing
Packing gland
Seal joint between cylinders
Has a wiper
Torque links
Keeps Pistons and wheels aligned
Retains the piston in the upper cylinder
Nose gear strut
Centering cam
Shimmy damper

## Slide 17: Struts
Nose gear
Locking or retaining pin for movement
Some aircraft can be rotated 360 degrees
Never exceed the limit lines on airframe
Jackin points
Towpoints
Instructional plate for servicing
On strut
Or in manual

## Slide 18: Strut Operation
Compression
Lower piston is forced into upper cylinder
Metering pin moves through orifice
Taper of the pin controls rate of flow
Heat is dissipated through the strut
At the end of compression air is compressed limiting stroke
Air in strut and tires provide cushion while taxiing
Insufficient fluid could cause bottoming out
Retraction
Fluid is forced by air back into the lower portion of the strut
Orifices and snubbers control fluid return
Sleeve, spacer, or bumper ring limits extension stroke

## Slide 19: Strut Servicing
Proper fluid quantity and air pressure should be maintained
Strut servicing can be dangerous
Pressure in strut can cause injury
Ensure you are familiar with valve types and operation
Two common valves are the
AN 6287-1 Rated at 3000 psi, core is rated at 2000 psi
MS28889-1 Valve has no core and is rated at 5000 psi
Both have a valve body hex

## Slide 20: Servicing Shock Struts
Position aircraft on ground free of stands, jacks and equipment
Remove cap from servicing valve
Check swivel nut for security
Release air pressure under valve core ensuring you are clear incase of failure
Loosen swivel nut slowly and release air
Remove entire valve assembly
Ensure strut is fully compressed
Fill to top with fluid
Re install valve with approved packing and torque to specs
Service with air as per the manufacturers specifications
Once inflated tighten swivel nut and torque
Remove fill hose and replace cap on valve

## Slide 21: Bleeding Shock Struts
If air become trapped in strut bleeding is required
Can be caused by low hydraulic fluid in the strut
Usually performed with aircraft on jacks
Attach bleed hose to valve
With gear fully extended open valve and release air pressure
Remove valve assembly
Fill strut with approved fluid
Attach hose to servicing port and insert end of hose into container filled with fluid
Use exerciser jack and cycle strut
Let strut extend on its own
Lower aircraft
Remove bleed hose
Install air valve
Inflate strut

## Slide 22: Landing Gear Alignment