## Slide 1: Aircraft landing gear systems
Airframe 02

## Slide 2: Section Overview
Landing Gear Types
Jacking
Wheel Alignment
Retraction Systems
Shimmy Dampeners
Landing Gear Struts
Wheels
Tires
Brakes

## Slide 3: Landing Gear Types
Numerous Configurations
Fixed
Retractable
Non-Shock Absorbing
Shock Absorbing
Amphibious
Skiis

## Slide 5: Gear Arrangements
Tail Wheel
Known as conventional gear due to many early aircraft having this configuration
Main gear is located forward of center of gravity
Tail gear or skid
Facilitated clearance for large props
Good for non-paved surfaces
Weight saving due light tail wheel
Differential braking and steering

## Slide 6: Gear Arrangements
Tandem landing gear
Main and tail aligned on longitudinal axis
Some have outriggers

## Slide 7: Gear Arrangements
Tricycle gear
Most commonly used
Used on large and small aircraft
Two mains and a nose gear
Benefits include
Enables higher landing speeds
Better visibility from flight deck
Prevents ground looping of aircraft

## Slide 8: Nose Gear
Can be non-controllable
Most are controllable with linkage or hydraulics
Heavy aircraft use an independent tiller

## Slide 9: Main Gear
Attached to a reinforced wing structure
Number of wheels vary
Multiple wheels spread load and provide backup
Bogie is when more than two wheels attached to a strut

## Slide 10: Tricycle Gear Components

## Slide 11: Fixed and Retractable Gear
Fixed
Small aircraft
Parasite drag
Wheel fairings
Fixed vs. retractable weights
Faster aircraft need to retract gear
Aerodynamic designs
Retractable
Stows gear in fuselage
Can be used to slow aircraft

## Slide 12: Shock and Non-Shock Absorbing
Forces on aircraft during landing must be controlled
Either by transfer through the airframe or by converting energy into heat energy
Leaf spring type
Gear flexes and returns to normal
Made from composite materials, lighter and do not corrode
Rigid
Direct transfer to airframe
Tires cushion landing
Helicopter skids
Bungee Cord
On non shock absorbing gear
Made of elastic rubber

## Slide 13: Shock Struts
Used to convert the energy of impact to heat through dissipation
Self contained hydraulic units
Must be inspected and service routinely
Uses compressed air or nitrogen combined with fluid
Air/oil strut or OLEO
Telescoping
Metering orifice
Metering pin
Heat is dissipated through the strut assembly
Some struts use metering tubes rather than pins
Snubbers or dampeners extension stroke

## Slide 15: Strut Parts
Axle
Provides installation of aircraft wheels
Struts without integral axle have provisions
Valve fitting assembly
Provides means of servicing
Packing gland
Seal joint between cylinders
Has a wiper
Torque links
Keeps Pistons and wheels aligned
Retains the piston in the upper cylinder
Nose gear strut
Centering cam
Shimmy damper

## Slide 17: Struts
Nose gear
Locking or retaining pin for movement
Some aircraft can be rotated 360 degrees
Never exceed the limit lines on airframe
Jackin points
Towpoints
Instructional plate for servicing
On strut
Or in manual

## Slide 18: Strut Operation
Compression
Lower piston is forced into upper cylinder
Metering pin moves through orifice
Taper of the pin controls rate of flow
Heat is dissipated through the strut
At the end of compression air is compressed limiting stroke
Air in strut and tires provide cushion while taxiing
Insufficient fluid could cause bottoming out
Retraction
Fluid is forced by air back into the lower portion of the strut
Orifices and snubbers control fluid return
Sleeve, spacer, or bumper ring limits extension stroke

## Slide 19: Strut Servicing
Proper fluid quantity and air pressure should be maintained
Strut servicing can be dangerous
Pressure in strut can cause injury
Ensure you are familiar with valve types and operation
Two common valves are the
AN 6287-1 Rated at 3000 psi, core is rated at 2000 psi
MS28889-1 Valve has no core and is rated at 5000 psi
Both have a valve body hex

## Slide 20: Servicing Shock Struts
Position aircraft on ground free of stands, jacks and equipment
Remove cap from servicing valve
Check swivel nut for security
Release air pressure under valve core ensuring you are clear incase of failure
Loosen swivel nut slowly and release air
Remove entire valve assembly
Ensure strut is fully compressed
Fill to top with fluid
Re install valve with approved packing and torque to specs
Service with air as per the manufacturers specifications
Once inflated tighten swivel nut and torque
Remove fill hose and replace cap on valve

## Slide 21: Bleeding Shock Struts
If air become trapped in strut bleeding is required
Can be caused by low hydraulic fluid in the strut
Usually performed with aircraft on jacks
Attach bleed hose to valve
With gear fully extended open valve and release air pressure
Remove valve assembly
Fill strut with approved fluid
Attach hose to servicing port and insert end of hose into container filled with fluid
Use exerciser jack and cycle strut
Let strut extend on its own
Lower aircraft
Remove bleed hose
Install air valve
Inflate strut

## Slide 22: Landing Gear Alignment
Purpose is for handling and tire wear
Set by manufacturer and seldom needs attention except after a hard landing
Toe-in or Toe-out –amount of angle on a longitudinal axis
Camber – amount of angle due to the vertical axis
Caster – rotational axis in relation

## Slide 24: Alignment Components
Torque links or arms – keeps lower strut cylinder from rotating out of alignment with the longitudinal axis of the aircraft
In some aircraft it is the sole means of holding the piston in the bore
Links attach to upper cylinder and bottom cylinder allowing the strut to compress or retract

## Slide 25: Gear Support
Gear is attached to wing spars or other structural members
Retractable gear must be designed to be able to move and withstand force
Trunnions are an example of how gear is attached to the airframe
Must have a drag brace to support gear when extended
Some use an over-center action to lock gear
Most use hydraulic locks

## Slide 26: Small Aircraft Retraction Systems
Aircraft reach a speed where parasite drag is more than the loss of performance due to retractable gear weight
Simple systems use a handle with gears and chains to reduce required force
Electrically operated gear is common converting rotary to linear action

## Slide 27: Electric/Hydraulic System
Known as a powerpack system
Pack contains several components of a hydraulic system

## Slide 28: Large Aircraft Retraction Systems
Always powered by hydraulics
Use of valves to operate various components

## Slide 29: Emergency Extension Systems
Lowers gear if main power fails
Gear can be extended by gravity or aided by pneumatic power
Uplocks are released by a mechanical connection or by pneumatics
Free fall valve is opened and fluid is released
Airflow lowers gear
Large aircraft high performance aircraft use a secondary system to actuate gear

## Slide 30: Landing Gear Safety Devices
There are numerous gear safety devices
Most are for gear on the ground
Also used to indicate to the pilot gear status
Nose wheel centering device
Safety switch
Wired to numerous circuits
Prevents gear from being raised on the ground
Lockout can be achieved in many ways
One is a solenoid that extends through the gear handle
Electromagnetic sensors can be used, good for used in dirty areas

## Slide 32: Landing Gear Safety Devices
Ground locks can also be used as added security
Could be as simple as a pin
Some are clamshell type
Must have red flag attached
Commonly carried with aircraft

## Slide 33: Position Indicators
Located on the instrument panel close to the gear handle
Inform the pilot on gear status
Green light usually indicate safe to land, lights out indicates gear up and locked
Transit lights could be barber poles, blinking lights or annunciator
Gear door position can also be monitored

## Slide 34: Nose Wheel Centering
Alignment before retraction
Centering cams built into the shock strut
When weight is on wheels cam is not functional
Some aircraft incorporate a small guide pin or roller on the gear to align with a track which straightens the gear.

## Slide 35: Landing Gear Maintenance
Moving parts and dirty environment of the landing gear make this an area of regular maintenance
Stresses on gear and supporting areas
A in depth inspection of the area is essential
Thoroughly clean the area before inspection
Ensure all ground locks are installed

## Slide 36: Areas of Interest
Emergency control handles and systems
Wheels
Tie bolts
Anti-skid wiring for deterioration
Tires for wear, cuts, deterioration, grease, oil, alignment
Gear condition and proper adjustment
Steering cables for wear
Brake clearances and wear

## Slide 37: Lubrication
By hand or grease gun
Follow instructions
Clean fittings before and after servicing
Clean piston rods
Wheel bearings must be removed, cleaned, inspected, and lubricated
Use recommended cleaning solvent
Do not use gas or jet fuel
Dry by using air between rollers
Do not spin the bearing with air
Inspect for wear
Lubricate immediately after cleaning and inspection to prevent corrosion
Use bearing lubrication tool or palm of hand method

## Slide 38: Rigging and Adjustment
Checking mechanisms for proper operation
Doors
Actuators
Locks
Switches
Latches

## Slide 39: Gear Latches
Normally used to hold gear up or down
Also used to hold doors open or closed
Must operate at the proper time and position
Clearances and tolerances must be checked
Usually composed of a latch cylinder, hook, spring loaded crank and lever, hook
Locked by a spring and unlocked by pressure
Cables are attached for emergency

## Slide 40: Clearances
An example of inspection of clearance on a door roller

## Slide 41: Gear Door Clearances
Clearances between doors and fuselage must be maintained
Adjustments are normally made on connecting links
Doors that close to tight can cause structural damage
Too loose can cause wear, failure and parasite drag

## Slide 42: Drag and Side Brace Adjustment
Proper adjustment of drag braces is crucial
Over center locking braces need to be checked for proper extension
Down lock spring tension must also be tested

## Slide 43: Landing Gear Retraction Test
Proper functioning of gear components can be tested by doing a retraction test
Lubricate prior to swinging gear
Close visual inspection should be performed
The emergency extension system should also be checked
General type inspection
Check for proper extension and retraction
Check all switches, lights, and warning devices for proper operation
Check the landing gear doors for clearance and freedom from binding
Check landing gear linkage for proper operation, adjustment and condition
Check the alternate/emergency extension or retraction systems for operation
Investigate any usual sounds, such as those caused by rubbing, binding, chafing, or vibration

## Slide 44: Nose Wheel Steering Systems
Most aircraft are steerable from the cockpit
Some have caster type steering using differential braking
Small aircraft have a simple cable system connected to the rudder pedals

## Slide 45: Large Aircraft Steering
Due to large mass a power source is needed for steering
Hydraulics dominate most systems
Usually controlled from the flight deck via tiller controls
An accumulator keeps pressure on steering cylinders at all times
Cylinders also act as shimmy dampers
Many systems have a input from the rudder pedals for minor corrections under high speed conditions
Safety valves are present allowing for movement during a hydraulic failure

## Slide 47: Shimmy Damper
Nose gear has a tendency to oscillate rapidly
This movement must be controlled by dampening
A hydraulic shimmy damper is installed
Can be integral, but most of the time it is independent
Operational during all ground operations

## Slide 48: Steering Damper
Large aircraft use steering cylinders to hold pressure
Some older aircraft use vane-type dampers
They function to steer the nose wheel as well as dampen vibration

## Slide 49: Piston Type
Aircraft without hydraulic steering use a piston type shimmy damper
Bleed hole dampens the vibrations
May contain a fill point or be a sealed unit
Check for leaks and fill to capacity

## Slide 50: Vane Type
Chamber with vanes and orifices
Steering can only change as fast as the fluid goes through the orifices
Spring loaded reservoir keeps the chamber full
Check for leaks and check the fluid indicator

## Slide 51: Non-Hydraulic Shimmy Damper
Currently certified for many aircraft
Similar look and fit as regular shimmy dampers
They contain no fluid inside
A rubber piston presses on the inner diameter of the bore
Piston is greased and proves resistance to movement
Also called surface effect dampening
Long service life without a need for adding fluid

## Slide 52: Aircraft Wheels
Important component of a landing gear system
Typical wheel is lightweight, strong, and made from aluminum alloy
Early wheels were of single piece construction
Aircraft wheels were made stiffer and stronger for more extreme conditions
Split wheels were needed to allow mounting since stretching a tire over rim was not possible
Early wheels were made with a removable flange

## Slide 53: Aircraft Wheels
Wheels support the entire aircraft through taxi, takeoff and landing
Lightweight, strong, and made from aluminum or magnesium alloy
Early wheel were single piece construction
Stiffer tires led to a flange type wheel and eventually to split rim

## Slide 54: Wheel Construction
Cast or forged from aluminum or magnesium alloy
Halves are bolted together with a seal in between for rims without tubes
Bead seat is where the tire actually touches the wheel
Bead area is rolled to prestress the area since it takes the load

## Slide 55: Inboard Wheel Half
Halves are not identical
Inboard half must have provisions for rotors of aircraft brakes
Both halves have a bearing seat
Thermal plugs are on the inboard half of high performance aircraft
Melt at a lower temperature than the wheel material
If plug melts tire must be removed from service and wheel must be inspected
Adjacent wheels must be inspected
Over inflation plug may also be installed on inboard wheel half
Fill valves are commonly placed on the inner half with stem going through to outer half

## Slide 56: Outboard Wheel Half
Bolts to inboard half
Has a bearing cup
Houses bearing cup or wheel transducer

## Slide 57: Wheel Inspection
On aircraft
Inspect for signs of suspected damage
Off aircraft
More in depth inspection may be performed
Proper installation
Gear is in a hostile environment
Installation should not be taken for granted
Wheel tie bolts and nuts
Missing bolt requires removal
Dust cap and anti-skid sensor
Inner half should interface with brake disk All brake keys must be present and secure
Cracks
Flaked paint

## Slide 58: Axle Nut Torque
Of extreme importance
Too loose can cause bearing cups to loosen and spin
Too tight distributes load improperly on bearing
Higher heat due to friction

## Slide 59: Off Aircraft Wheel Inspection
A thorough inspection means removal of the tire from the wheel
Observe the following caution when removing wheel from aircraft
Deflate tire before loosening the axle nut
Let tires cool before removal (three hours or more)
Do not stand in the trajectory of the valve core
Remove only one of a pair of tires at a time incase aircraft falls from jacks

## Slide 60: Loosening Tire from the Rim
After usage the tire tends to adhere to the wheel
Bead must also be broken
Mechanical and hydraulic presses can be used to remove bead
Ensure air is removed
Never pry with screwdriver
Wheels are relatively soft, damage can lead to failure

## Slide 61: Disassembly of the Wheel
Should be done on a clean area on a flat surface
Remove bearings first
Remove tie bolts
Do not use impact tools for tie bolts
Wheels are not designed to take impact

## Slide 62: Cleaning the Wheel
Clean with solvent recommended by manufacturer
Use soft non-metallic brush
Clean wheels can be dried with compressed air

## Slide 63: Cleaning the Wheel Bearings
Bearings should be removed and cleaned with aliphatic naphtha, varsol, or Stoddard solvent.
Soaking is acceptable
Brushed clean and dried with compressed air
Never rotate bearing when using compressed air
Can come apart
Can deteriorate surface finishes

## Slide 64: Wheel Bearing Inspection
Nearly all flaws discovered in a bearing are usually grounds for replacement
Common conditions:
Galling - rubbing of mating surfaces, destroys surface

## Slide 65: Wheel Bearing Inspection
Spalling - a chipped away portion of a hardened surface
Overheating – caused by lack of lubrication
Brinelling – Caused by excessive impact, static overload
or severe impact

## Slide 66: Wheel Bearing Inspection
False brinelling – static load causing corrosion (frictional corrosion)
rust colored lubricant
Staining – water that has gotten into the bearing
Etching and corrosion – water damage that penetrates
surface treatment
Bruising – particle contamination due to worn seals

## Slide 67: Wheel Bearing Inspection
Spinning bearing cup

## Slide 68: Bearing Handling and Lubrication

## Slide 69: Aircraft Brakes
Very early aircraft had no brakes
Used slow speeds, soft fields and tail skid
Faster aircraft needed a brake system
Hold aircraft stationary, stop aircraft, allow for turning on the ground
Main wheels are equipped with brakes
Typical brakes are controlled by pressing on the top of the rudder pedals
Kinetic energy is turned into heat energy during braking
Proper adjustment, maintenance, and inspection of the brake system is essential

## Slide 70: Types of Aircraft Brakes
Modern aircraft typically use disk brakes
Disk rotates with wheel
Caliper is fixed and resists rotation when applied
Size, weight and complexity dictates the type of brake system
Single, dual, and multiple disk brakes are common
Segmented rotors are used on larger aircraft
Expander tube brakes are found on older aircraft
Carbon disks are increasingly being used

## Slide 71: Single Disc Brakes
Small aircraft usually have a single disk bolted or keyed to wheel
Caliper presses on disk via brake pads
Hydraulic master cylinders are connected to each rudder pedal

## Slide 72: Floating Disk Brakes
Caliper straddles the disk
Three cylinders bore in caliper
Pucks in each
When pressure is applied and released springs move piston away from disk
Spring maintains a preset clearance between disk and pucks
Self adjusting feature maintains the same clearance regardless of wear on pucks
A piston that contacts the pucks serves as a wear indicator
Caliper has passages drill in it for fluid travel
Also has bleed port for servicing

## Slide 73: Fixed Disk Brakes
Disk is bolted to wheel and caliper floats
Common on light aircraft
Cleveland brake company manufactures this type of brake
Linings adjust in relation to the disk
Liners are riveted to backing plate
Cleveland brake liners can be replaced without removing the wheel
Bolts allow the caliper to be removed free of the disk

## Slide 74: Dual Disk Brakes
Two disks are keyed to wheel instead of one
Used when single disk does not provide sufficient braking
Center carrier is located between two disks
Mounting bolts are long and go through the carrier

## Slide 75: Multiple Disk Brakes
Large, heavy aircraft use these type of brakes
Heavy duty with power brake controls and boosters
An inner piston causes the entire stack to compress
Enormous friction is applied slowing the rotation of the wheel
Springs retract assembly when brakes are released
Adjuster traps a certain amount of fluid to provide correct clearances
Wear is measured with external measuring equipment
Disks are 1/8 inch thick and can warp

## Slide 77: Segmented Rotor Disks
Developed to dissipate heat more efficiently
Improvement over multiple disk brakes
Rotors are constructed with slots for cooling

## Slide 78: Carbon Brakes
40 percent lighter than conventional brakes
Can withstand temperatures 50 time that of steel
Dissipate heat faster
Maintains strength and dimensions at high temperatures
High priced

## Slide 79: Expander Tube Brakes
1930-50’s
Tube moves outward and makes contact with drum
Springs return tube to normal size
They tend to take setback when cold
They swell with temp and leak
Drag may occur

## Slide 80: Brake Actuating Systems
Means of delivering hydraulic fluid to brake assemblies
Independent system
Can have a booster system that uses aircraft hydraulic system

## Slide 81: Independent Master Cylinders
Not connected in any way to the aircraft hydraulic systems
Master cylinders are used to develop pressure
Tops of rudder pedals

## Slide 82: Independent Master Cylinders
Some aircraft have single reservoir that feed the both master cylinders
Common on aircraft with nose wheel steering
Master cylinder builds up pressure for operation

## Slide 83: Independent Master Cylinders
Always filled with air free fluid
Pushes against fluid to actuate brakes
Spring returns system to non-actuated position
Temperature increases can cause dragging so a compensator port is installed
Allows for fluid to expand safely when brakes are not actuated