## Slide 1: Hydraulic Systems

## Slide 2: Basic Aircraft Hydraulic Systems
Must have several basic components
Fluid to transmit force
Reservoir to hold the fluid
Pump to move fluid
Actuator to exchange the flow of fluid to mechanical work
Lines to carry fluid
Valves to control the flow and pressure of fluid
Additional components to increase efficiency

## Slide 3: The Basic Brake System
Sealed brake system

## Slide 4: Brake System
Reservoir-type brake system

## Slide 5: Open Center Hydraulic System
Limit complexity on small and medium size aircraft
Hose fluid flow rather than pressure
No pressure regulator installed
Selector valves installed in series
Once actuation is complete valve returns to open-center
Limited load on the pump

## Slide 7: Closed Center Hydraulic System
Fluid is under pressure
Actuators are arranged in parallel
Pressure control depends upon pump type
Constant delivery pump requires regulator and relief
Variable displacement pump has internal compensator
More abrupt operation due to constant pressure
Good for application where instant operation is required
http://www.allstar.fiu.edu/aero/Hydr02Aanim.htm
Notes: Start Here

## Slide 9: Evolution of The Hydraulic System
First used for brakes
Then control systems
Now in use are “Power pack” systems

## Slide 10: Hydraulic “Power Pack” Systems
Small unit with pump, filters, reservoirs, valves
No need for centralized system
Either gearbox or electric motor driven
Reduces weight
Virtually eliminates external leakage
Controls systems directly

## Slide 11: Hydraulic System Components

## Slide 12: Reservoirs
Stores fluid and provides expansion space
Removes air from fluid
Supplies fluid for operating needs of system
Replaces fluid lost to leaks
Separates foreign matter via strainers
Some have internal traps for negative “G” conditions
Main system draws from a standpipe
Emergency system draws from the bottom

## Slide 13: Two Common Types of Reservoirs
Nonpressurized
Low altitude, non violent maneuvers, located in pressurized area
Cylindrical in shape
Vented to the atmosphere via check valve
Sight gauge, possible fluid quantity gauge in cockpit
Slightly pressurized due to thermal expansion and return

## Slide 15: Pressurized Reservoir
Air-pressurized
Used on most commercial transport high altitude A/C
Compressor bleed air is used to pressurize
Venturi air is used to pressurize
Cylindrical shape
Sample port, drain valve, sight gauge, transducers (quant/temp)
May have a pressurization module (pg. 12-11, 8083)

## Slide 18: Pressurized Reservoir
Hydraulic Pressurized
Pump pressure is applied to movable piston
Piston pushes against fluid
Provides head pressure for high altitudes
Protruding piston indicates quantity
3000 PSI will create 30 PSI reservoir pressure when the area of the large piston is 100 times the small piston

## Slide 20: Reservoir Servicing
Non-pressurized can be serviced by pouring through a strainer on top or a service port
Pressurized usually have a central filling station
Pressure fill port for mule or servicing cart (flush)
Hand pump with selector valve

## Slide 21: Video Time
Airbus (10min)
http://www.youtube.com/watch?v=7RAbiYpN_v4
Notes: Start

## Slide 22: Filtration
High pressures and close tolerances require clean systems
Contaminants are measured in microns
Human eye can see 40 micron particle
Most systems filter out to 3 microns
Patch testing can reveal contamination
One micron is one-millionth of a meter

## Slide 24: Filters
Screening or straining device
Picks up particle from normal wear of components
Can be located in any location that filtering is needed
Come in two types (Surface and edge(cuno))
Composed of three basic units

## Slide 25: Filter Bypass (PDI) Indication

## Slide 26: Surface Filter Elements
Trap contaminates on surface
Fiber elements are not cleanable
Most metal elements are cleanable

## Slide 27: Edge Filter Elements
Commonly know as “Cuno”filters
Stacks of thin metal disks with scrapers between them
Contaminates are collected on the edge of disks
Degree of filtration depends upon separator size
Cleaned by turning shaft actuating the scrapers
Contaminates can then be drained by empting bowl

## Slide 28
http://www.youtube.com/watch?v=VxLTDtaRCZk

## Slide 29: Hydraulic Pumps
All aircraft hydraulic systems have one or more power driven pumps.
Engine driven, electric motor driven, or air driven
Electric motors are more commonly used for emergencies and ground operations
Ram air turbine

## Slide 30: Hand Pumps
Used for operation of subsystems and testing
Can also be used for emergencies
Servicing from a collective source
Two types
Single and double

## Slide 31: Power driven pumps
Many are variable delivery with some being constant
Both operate similarly

## Slide 32: Classification of PUMPS
Either positive displacement or nonpositive displacement
Nonpositive produces a continuous flow but varies in pressure ouput
Centrifugal and propeller pumps are examples

## Slide 33: Constant displacement pump
Forces a fixed unvarying amount of fluid through the outlet for each revolution
Also referred to as constant volume or displacement pumps
RPM determines output
Must have a pressure regulator

## Slide 34: Gear type power pump
Constant delivery pump
Very small clearance between gears

## Slide 35: Gerotor pumps
Housing containing an eccentric shape liner
Partial vacuum draws fluid
Narrowing space expels fluid

## Slide 36: Piston pump
Can be positive displacement or variable displacement
Multi bore cylinder block
Piston for each bore
Valve plate with inlet and outlet slots
Most have a shear shaft

## Slide 37: Bent axis piston pump
Bent axis configuration provides varied piston pump

## Slide 38: Vane pump
Constant displacement
Four blades and rotor positioned off center

## Slide 39: Variable-displacement pumps
Varied pressure to meet the demands of the system
Output is controlled by an internal compensator

## Slide 40: Normal pumping mode
Compensator is held closed by spring
When pressure setting is exceeded spool lets fluid into the piston
Decreasing demands causes the outlet pressure to increase and admit fluid to actuator
Reduced angle/shorter stroke

## Slide 41: Depressurized mode
Compensator valve closes and connects the actuator to pump outlet
Used to reduce engine load on startup
Also used to take pump offline in multiple pump systems for testing

## Slide 42: Review
Study required reading for this section, review notes, and study quizzes.