## Slide 1: Hydraulic Systems Valves

## Slide 2: Flow Control Valves
Control speed and direction of flow
Examples
Selector valves
Check valves
Sequence valves
Priority valves
Shuttle valves
Quick disconnect valves
Hydraulic fuses

## Slide 3: Selector Valves
Controls movement of hydraulic actuator or similar device
Provides simultaneous flow within unit

## Slide 4: Types of Selector Valves
Poppet
Spool
Piston
Rotary
Plug

## Slide 5: Open and Closed Center Valves
Open- allows continuous flow of fluid
Closed-shuts flow off when in neutral or off position
Most common used in aircraft hydraulic systems

## Slide 6: Servo Controlled Selector Valve
Energized using electrical solenoids

## Slide 7: Check Valves
Allows unrestricted flow in one direction
Can be in-line or within component (Integral type)
Spring flapper, ball or piston

## Slide 8: Orifice-Type Check Valves
Full fluid flow in one direction restricted in the other
Also called a dampening check valve
Contains calibrated machined orifice
Used in landing gear mostly to dampen movement

## Slide 9: Sequence Valves
Controls the sequence of operation between two branches of a circuit
Landing gear doors and gear
Controlled by pressure, mechanical, or electrical circuits

## Slide 10: Pressure Sequence Valve
Actuated by pressure
Once one operation is complete the pressure opens piston to energize other
Drain incorporated for passing fluid

## Slide 11: Mechanical Sequence Valves
Plunger actuated through the body of the valve
Plunger is actuated by the primary unit
Check valve unseated by pressure or plunger

## Slide 13: Priority Valves
Prioritizes systems when pressure is low
Non-critical systems are bypassed at a set pressure

## Slide 14: Quick Disconnect Valves
Installed in lines to prevent fluid loss
Used in both pressure and suction lines immediately upstream and downstream of pumps
Allows test stand connection
Valve has a poppet type assembly

## Slide 15: Hydraulic Fuses
Safety device to cutoff flow
Detects a sudden increase in flow , burst downstream
Preserves fluid for the rest of the system
Uses
Brake systems
Flaps and slats
Gear
Thrusters
Also comes in an automatic reset configuration

## Slide 16: Pressure Control Valves
A means to control pressure for safe and efficient operations
Various types and uses
Escape for pressure above set limit
Reducers
Maintain system pressures

## Slide 17: Relief Valves
Regulates pressure for system requirements
Limit amount of pressure on a confined liquid
Protects components
Protects lines from rupture
A safety valve that can be adjusted in some cases
Fluid discharges to return line
Various types
Ball
Sleeve
Poppet

## Slide 18: Relief Valves
System relief valve
Used as safety device to back up pressure regulators or pump compensators
All systems with hydraulic pumps have relief valves as safety devices
Thermal relief valve
Used to relieve pressure due to thermal expansion
Used when a check valve or selector valve prevents pressure from being relieved via main system valve
Usually smaller than system relief valves

## Slide 19: Pressure Regulators
Used with constant-delivery pumps
Manages the output within predetermined range
Allows the pump to turn without resistance
Position before the system and after pump
The combination of pump and regulator is the same as a variable delivery type pump

## Slide 20: Pressure Reducers
Lower normal operating by specified amount
Supplies pressure to a system that operates at a lower pressure
A reducing valve can normally be set for any desired pressure
Once set pressure is maintained regardless of changes in supply (as long supply is higher)

## Slide 21: Shuttle Valves
Main purpose is to isolate normal system from an alternate or emergency system
Shuttle shuts off flow to normal system when spring pressure is overcome
Four types
Sliding plunge
Spring-loaded piston
Spring-loaded ball
Spring-loaded poppet

## Slide 22: Shutoff Valves
Used primarily to shutoff flow
Can be used to prioritize flow

## Slide 23: Accumulators
Steel sphere divided into two chambers by a diaphragm
Upper chamber contains fluid at system pressure
Lower chamber is charged with nitrogen
Cylindrical types can be used in high pressure systems
Many Aircraft may have multiple accumulators/main system and emergency system

## Slide 24: Spherical Accumulator
Two halves fastened, threaded or welded together.
Top port and bottom port
Air side has Schrader valve
Synthetic rubber bladder or diaphragm
Screen to prevent extrusion
Bladder is installed using a retainer plug

## Slide 25: Cylindrical
Cylinder and piston assembly
Sealed with gaskets and packings

## Slide 26: Accumulator Operation
Accumulator is pre-charged with nitrogen (accumulator preload)
Preload must be overcome to move piston or bladder
Used to augment or operate systems
http://www.epa.gov/otaq/technology/research/videos/bladder_accumulator.webm
http://www.slideshare.net/YsPrasanna/aircraft-hydraulic-systems

## Slide 27: Maintenance
Inspection, minor repairs, replacement of parts and testing
They can be dangerous
Before disassembling ensure all pressure is bled off
Ensure your familiar with the operation of the valve used to fill and empty unit

## Slide 28: Heat Exchangers
Used in transport type aircraft
Cools fluid extending service life to components and fluid
Can be located within fuel tanks
Constructed of aluminum finned tubes to transfer heat

## Slide 29: Actuators
Transforms fluid energy into mechanical energy
Imparts linear motion on an object or mechanism
Parts
Cylinder Housing
Piston and rods
Seals
Two major types
Single-action
Double action

## Slide 30: Single-Action Actuator
Single port produces power only in one direction
Controlled by a three-way selector valve

## Slide 31: Double-Action Actuator
Provides power in both directions
Controlled by a four-way selector valve
Has ability to hold a load in position

## Slide 32: Linear Actuator Operation

## Slide 33: Rotary Actuators
Can be mounted right at the part within a limited space
Varied in configurations, not limited to 90 degree pivot arc
Rack and pinion design used for many nose wheel steering systems

## Slide 34: Hydraulic Motors
Piston type are most common
Same design as a pump except they convert hydraulic energy to mechanical energy
Either axial inline or bent axis type
Most common is fixed-displacement bent axis
Used on flaps, slats, and trim
Some may be of variable-displacement
Advantages
Constant efficient speed
Rapid/smooth operation
Control over max torque/power
Smooth reverse operation