## Slide 1: Aircraft PNEUMATICS
Airframe 02

## Slide 2: Pneumatics Background
Systems of the past used up to 3000 PSI for various purposes
Brakes
Opening and closing doors
Driving hydraulic pumps
Emergency device operation
Both pneumatic and hydraulic systems used confined fluids
Main difference is compressibility
Both can be used to transmit power
The type of unit used depends on system requirements

## Slide 3: High Pressure Systems
Usually stored in metal bottles 1000-3000 PSI
Has two valves
Control valve for operation of system also a shutoff valve
Charging valve for pressurizing system

## Slide 4: High Pressure Systems
Can be stored in a light weight cylinder
Drawback is the system cannot be charged in flight
Most systems are used for emergency operations
Can be used indefinitely in flight if a pump is installed

## Slide 5: System Components
Similar to hydraulic system components
Air Compressors – Permanently installed if recharge in flight is needed. Two to three stage compression depending on requirements
Relief Valves – Used to prevent damage to seals and lines due to
overpressure
Control Valves – Used to control air movement, three port housing,
poppet valves, control lever with lobes
Check Valves – One direction flow control valve

## Slide 6: System Components
Restrictors – Type of control valve similar to an orifice check valve
Variable Restrictor – Adjustable speed regulating unit

## Slide 7: Filtration
Protects system for contamination
Micronic filter has a housing and two ports, an element and a relief valve
When filter is clogged relief valve opens
Screen type filters are permanent filters that can be clean by turning a handle

## Slide 8: Desiccant / Moisture Separator
Always downstream of the compressor
Reservoir
Pressure switch
Dump valve
Check valve
Separator reservoir is dumped by the pressure switch
Purges lines up to compressor
Check valve prevents pressure loss and reverse flow
Chemical Drier – Absorb moisture that collects in lines and system components
Usually blue in color

## Slide 9: Emergency Backup Systems
Used in landing gear and brake systems as a back-up
Not directly used in the system, but used to move fluid
Nitrogen Bottles – Released by actuation of outlet valve
Must be refilled on ground
Outlet valve is connected to a cable and handle assembly
Handle can charge be used for extension and system dumping
Dump valve – Used to release nitrogen into system and isolate the gear system form the rest of the hydraulic system